## Slide 1: ARM

## Slide 2: RISC features
Instructions:
  Lower number of instructions compared to CISC.
    Each instruction is a fixed length to allow the pipeline to fetch future instructions before decoding the current instruction.
Pipeline:
  The processing of instructions is broken down into smaller units that can be executed in parallel by pipelines.
  Instructions can be decoded in one pipeline stage.

## Slide 3
Fixed number of instruction cycles:
  Most instructions single cycle.
Registers:
  RISC have a large number of general purpose registers while CISC have special purpose registers.
  In RISC any register can contain either data or an address. Registers act as the fast local memory store for all data processing operations.
Load-store architecture :
  The processor operates on data held in registers.
  Separate load and store instructions transfer data between the register bank and external memory.
  Memory accesses are costly, so separating memory accesses from data processing pro-vides an advantage because you can use data items held in the register bank multiple times without needing multiple memory accesses. In contrast, with a CISC design the data processing operations can act on memory directly.

## Slide 4: ARM feature improvements over RISC
Variable cycle execution for certain instructions:
  Not every ARM instruction executes in a single cycle. For example, load-store-multiple instructions vary in the number of execution cycles depending upon the number of registers being transferred. The transfer can occur on sequential memory addresses, which increases performance since sequential memory accesses are often faster than random accesses.
Inline barrel shifter leading to more complex instructions:
  The inline barrel shifter is a hardware component that preprocesses one of the input registers before it is used by an instruction. This expands the capability of many instructions to improve core performance and code density.

## Slide 5
ARM has enhanced the processor core by adding a second 16 bit instruction set called Thumb.
  This thumb instruction permits the ARM core to execute either 16 bit or 32 bit instructions.
  The 16 bit instructions improve code density by about 30 percent compare to 32 bit instructions of fixed length.
Conditional execution:
  An instruction is only executed when a specific condition has been satisfied. This feature improves performance and code density by reducing branch instructions.

## Slide 6
Enhanced instructions:
  The enhanced digital signal processor (DSP) instructions were added to the standard ARM instruction set to support fast 16 x 16-bit multiplier operations and saturation. These instructions allow a faster-performing ARM processor in some cases to replace the traditional combinations of a processor plus a DSP.

## Slide 7: Load-store architecture
Only load and store instructions access the memory, all other instructions use registers as operands.
What is the motivation?
  Primary motivation is speedup –registers are faster.
Load r1,A
Load r2,B
Add r3,r1,r2
Store C,r3
Let's look at the code for C = A + B

## Slide 8
The ARM is a Load / Store Architecture:
  Does not support memory to memory data processing operations.
  Must move data values into registers before using them.
This might sound inefficient, but in practice isn’t:
  Load data values from memory into registers.
  Process data in registers using a number of data processing instructions which are not slowed down by memory access.
  Store results from registers out to memory.
The ARM has three sets of instructions which interact with main memory. These are:
  Single register data transfer (LDR / STR).
  Block data transfer (LDM/STM).
  Single Data Swap (SWP).