## Slide 1: Introduction to Embedded Systems.
Shriram K Vasudevan
20/05/2016
Session – 1
Faculty Development Programme.

## Slide 2: Agenda
  Introduction to Embedded Systems
  Characteristics of Embedded Systems
  Components of Embedded Systems - OS Will come as a part
  OS – Heart of any system
  Difference between RTOS and OS.
  Queries.

## Slide 3: Lets define.
  What is a System ?
  Simple. Anyone can say! Input + processing + output.
  What is embedded system?
  Computing system other than desktop computers
  An embedded system is the one that has computer hardware with software embedded in it as one of its most important components
  It is any device that includes a programmable computer but is not itself intended to be a general purpose computer.
  Example will make life easier! Air conditioner!

## Slide 4: Characteristics of embedded systems
All Embedded Systems have certain common characteristics. They can be listed as follows:
  Single Functioned
  Tightly Constraint
  Real Time & Reactive
  Complex Algorithms
  User Interface
  Multi rate
  Manufacturing Cost
  Power
  Let’s see about all these in a detail.

## Slide 5: A Diagrammatic representation of Embedded Systems Architecture – Presented here!
SENSORS
KEY
SWITCHES
INPUT
A
C
Q
U
I
R
E
A
N
A
L
Y
Z
E
CO
N
T
R
O
L
D
I
S
P
L
A
Y
ACTUATORS
DISPLAYS
ALARMS
INDICATORS
OUTPUT
TYPICALLY : COMPARE, SIGNAL PROCESS (VOICE/PROCESS)

## Slide 6: A Diagrammatic representation of Embedded Systems Architecture – Presented here!
Sensors
KEY, SWITCHES, INPUTS
ACTUATORS, DISPLAYS, ALARMS, INDICATORS,
OUTPUTS
ACQUIRE
ANALYZE
(PROCESS)
DISPLAY
CONTROL
Compare Signal process
(Voice Image)
Communicate
Wired / Wireless/ Mobile

## Slide 7
Challenges in Embedded System Design
There are many challenges in designing an embedded system. Let us discuss them as follows in detail:
  How much hardware do we need?
  How do we meet deadlines?
  How do we minimize power consumption?
  How do we design for upgradeability?
  Does it really work?
  How does the nature of ES make their design more difficult?
  Does it optimize the design metrics?
Let’s pick each of the above challenges and discuss!

## Slide 8: Conflicting requirements
Metrics usually compete one with another, improving one will affect Other metric.
For example if we reduce size, it may affect performance.

## Slide 9: MUP Vs. MUC
Micro-Controller.

## Slide 10: Mup vs. MUC

## Slide 11: Risc Vs. CISC
On the right is a diagram representing the storage scheme for a generic computer.
The main memory is divided into locations numbered from (row) 1: (column) 1 to (row) 6: (column) 4.
The execution unit is responsible for carrying out all computations.
However, the execution unit can only operate on data that has been loaded into one of the six registers (A, B, C, D, E, or F).
Let's say we want to find the product of two numbers - one stored in location 2:3 and another stored in location 5:2 - and then store the product back in the location 2:3.

## Slide 12: Contd., THE CISC APPROACH
The primary goal of CISC architecture is to complete a task in as few lines of assembly as possible.
This is achieved by building processor hardware that is capable of understanding and executing a series of operations. For this particular task, a CISC processor would come prepared with a specific instruction (we'll call it "MULT")
When executed, this instruction loads the two values into separate registers, multiplies the operands in the execution unit, and then stores the product in the appropriate register. Thus, the entire task of multiplying two numbers can be completed with one instruction:
MULT 2:3, 5:2
MULT is what is known as a "complex instruction.“
It operates directly on the computer's memory banks and does not require the programmer to explicitly call any loading or storing functions.
It closely resembles a command in a higher level language
Because the length of the code is relatively short, very little RAM is required to store instructions.
The emphasis is put on building complex instructions directly into the hardware
Advantages:

## Slide 13: Contd., The RISC Approach
RISC processors only use simple instructions that can be executed within one clock cycle.
Thus, the "MULT" command described above could be divided into three separate commands:
      "LOAD," which moves data from the memory bank to a register
      "PROD," which finds the product of two operands located within the registers
      "STORE," which moves data from a register to the memory banks.
LOAD A, 2:3 LOAD B, 5:2 PROD A, B STORE 2:3, A
Is this less efficient?
More RAM is needed to store the assembly level instructions.
The compiler must also perform more work to convert a high-level language statement into code of this form.
Not actually, there are benefits!
These RISC "reduced instructions" require less transistors of hardware space than the
complex instructions, leaving more room for
general purpose registers.
Because all of the instructions execute in a
uniform amount of time (i.e. one clock),
pipelining is possible
Notes: more RAM is needed to store the assembly level instructions. The compiler must also perform more work to convert a high-level language statement into code of this form.

## Slide 14: So?

## Slide 15: Summary
System
Embedded System
Characteristics
Challenges
CISC Vs. RISC