## Slide 1: 15CSE301 Computer Organization and Architecture
Floating point representation
Arthmetic
Dr Ganesh Neelakanta Iyer
Amrita Vishwa Vidyapeetham, Coimbatore
Associate Professor, Dept of Computer Science and Engg
Reference:
Chapter 3
Computer Organization and Design, The hardware / software interface, 3rd Edition

## Slide 2: Integer Addition
Example: 7 + 6
§3.2 Addition and Subtraction
Overflow if result out of range
  Adding +ve and –ve operands, no overflow
  Adding two +ve operands
    Overflow if result sign is 1
  Adding two –ve operands
    Overflow if result sign is 0

## Slide 3: Integer Subtraction
Add negation of second operand
Example: 7 – 6 = 7 + (–6)
  +7: 0000 0000 … 0000 0111 –6: 1111 1111 … 1111 1010 +1: 0000 0000 … 0000 0001
Overflow if result out of range
  Subtracting two +ve or two –ve operands, no overflow
  Subtracting +ve from –ve operand
    Overflow if result sign is 0
  Subtracting –ve from +ve operand
    Overflow if result sign is 1

## Slide 4: Multiplication
Start with long-multiplication approach
1000
× 1001
1000
0000
0000
1000
1001000
Length of product is the sum of operand lengths
multiplicand
multiplier
product
§3.3 Multiplication

## Slide 5: Multiplication Hardware
Initially 0

## Slide 6: Optimized Multiplier
Perform steps in parallel: add/shift
One cycle per partial-product addition
  That’s ok, if frequency of multiplications is low

## Slide 7: Faster Multiplier
Uses multiple adders
  Cost/performance tradeoff
Can be pipelined
  Several multiplication performed in parallel

## Slide 8: MIPS Multiplication
Two 32-bit registers for product
  HI: most-significant 32 bits
  LO: least-significant 32-bits
Instructions
  mult rs, rt / multu rs, rt
    64-bit product in HI/LO
  mfhi rd / mflo rd
    Move from HI/LO to rd
    Can test HI value to see if product overflows 32 bits
  mul rd, rs, rt
    Least-significant 32 bits of product –> rd

## Slide 9: Division
Check for 0 divisor
Long division approach
  If divisor ≤ dividend bits
    1 bit in quotient, subtract
  Otherwise
    0 bit in quotient, bring down next dividend bit
Restoring division
  Do the subtract, and if remainder goes < 0, add divisor back
Signed division
  Divide using absolute values
  Adjust sign of quotient and remainder as required
1001
1000 1001010
-1000
10
101
1010
-1000
10
n-bit operands yield n-bit quotient and remainder
quotient
dividend
remainder
divisor

## Slide 10: Division Hardware
Initially dividend
Initially divisor in left half

## Slide 11: Optimized Divider
One cycle per partial-remainder subtraction
Looks a lot like a multiplier!
  Same hardware can be used for both

## Slide 12: Faster Division
Can’t use parallel hardware as in multiplier
  Subtraction is conditional on sign of remainder
Faster dividers (e.g. SRT devision) generate multiple quotient bits per step
  Still require multiple steps

## Slide 13: MIPS Division
Use HI/LO registers for result
  HI: 32-bit remainder
  LO: 32-bit quotient
Instructions
  div rs, rt / divu rs, rt
  No overflow or divide-by-0 checking
    Software must perform checks if required
  Use mfhi, mflo to access result

## Slide 14: Floating Point
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized

## Slide 15: Floating Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 16: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalize significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1023
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 17: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 18: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 19
Lec 14
Systems Architecture
19
Representation of Floating Point Numbers
IEEE 754 single precision
31
30
23
22
0
Sign
Biased exponent
Normalized Mantissa (implicit 24th bit = 1)
(-1)s  F  2E-127
Notes: September 4, 1997
19

## Slide 20: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 21: Show the IEEE 754 binary representation of the number 0.75ten in single and double precision

## Slide 22: Another example
Represent 7:
  Convert to binary: 111
  Normalize: 1.11×22
  Sign bit is 0
  Biased exponent is 127 + 2 = 10000001two
  Coefficient is 1100…0
0
10…01
11000000000000000000000000000

## Slide 23: Another example
Represent 1/2
  Convert to binary: 0.1
  Normalize: 1.0×2-1
  Sign bit is 0
  Biased exponent is 127 – 1 = 01111110two
  Coefficient is 00…0
0
01…10
00000000000000000000000000000

## Slide 24: Another example
Represent –2
  Convert to binary: 10
  Normalize: 1.0×21
  Sign bit is 1
  Biased exponent is 127 + 1 = 10000000two
  Coefficient is 00…0
1
10…00
00000000000000000000000000000

## Slide 25: Yet another example
Represent –2
  Convert to binary: 10
  Normalize: 1.0×21
  Sign bit is 1
  Biased exponent is 127 + 1 = 10000000two
  Coefficient is 00…0
1
10…00
00000000000000000000000000000

## Slide 26: Floating-Point Example
What number is represented by the single-precision float
11000000101000…00
  S = 1
  Fraction = 01000…002
  Exponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0

## Slide 28: T2 Answer Key
Question | S1 | S2
No of clock cycles by 5 stage pipeline to execute x instructions | 1*5+499 = 504 | 1*5+299 = 304
Time for non pipelined machine | 500*10*5 = 25000 ns | 300*15*5 = 22500 ns
Time for pipelined machine | 504*15 = 5040 ns | 304*15 = 4560 ns
Speedup ratio | 25000/5040 = 4.96 | 22500/4560 = 4.93
Clock cycles when not in pipeline | 500*5 = 2500 | 300*5 = 1500